## Slide 1: OPC - Early computers
PROGRAM-CONTROLLED COMPUTERS – These computers (1938-1949) were programmed by setting switches and inserting patch cables.
Primitive architecture –CPU, ALU, registers, I/O devices, storage units?, etc.,….
  Every configuration of switches and patch cables conformed an instruction. Each instruction was wired, then the program.
  The electric storage units and I/O devices ranged from very primitive to something better, for a short time.

## Slide 2: Context of a current Computer
Current architecture –CPU (control unit), ALU, registers, storage unit, I/O devices, etc.,….
VON NEUMANN’S –
  The addition of a stored-program in a single separate memory structure that keeps both instructions and data.
  The computers that follow the "von Neumann architecture" are also known as the "stored-program computer“.
Registers

## Slide 3: Hardware moderno con Bus
Componentes de una computadora básica
  Exceptuando el CPU, cada uno de los componentes tiene un controlador
  Cada controlador posee: registros y un buffer, para realizar las entradas y / o las salidas.
  El bus tiene tres canales: datos, direcciones de memoria y señales de control.
BUS
Monitor
controller

## Slide 4: A Desktop Computer with USB
BUS
controller

## Slide 5: Intel D850MD Motherboard
dynamic RAM
Pentium 4 socket
Speaker
IDE drive connectors
mouse, keyboard, parallel, serial, and USB connectors
AGP slot
Battery
Video
Power connector
memory controller hub
Diskette connector
PCI slots
I/O Controller
Firmware hub
Audio chip

## Slide 6: Computer System Components (layers)
Command Interpreter?
Kernel
Instructions?
Software
O.S.
Basic Routines

## Slide 7: Computer System Components
Users (people, machines, other computers)
System and Applications programs : System programs – help the users to develop applications (compilers, assemblers, database systems, line text editors, etc.), Command Interpreter. Applications programs – help the users to solve their computing problems (spreadsheets, web explorers, video games, business programs, word processors, function libraries). -Software-.
Basic Routines – controls and coordinates the use of the hardware among the various application programs for the various users. For these tasks contains programs and subprograms (kernel) -Software-.
Hardware – provides basic computing resources (CPU, memory, I/O devices)

## Slide 8: Computer Hardware
Which ones are the main functions / services of the Computer Hardware?
  __________________
  __________________
  __________________

## Slide 9: Referencias
Chapters: Tanenbaum, Operating Systems.
Notas de Ramón Ríos.
13-Ago-2018